## Slide 1: Memory Module
Memory
Module
CLK
CS
WE
RESET
Address [15:0]
Data [7:0]

## Slide 2: Memory Module
﻿﻿module TOP_MESTProMem3
#(
parameter ADDR_BITS = 16, DATA_BITS = 8, MEM_SIZE = 2**ADDR_BITS, ROM_SIZE = 2048
)
(
input wire [ADDR_BITS-1:0] addr,
input wire [DATA_BITS-1:0] in_dat,
input wire CLK,
input wire WE,
input wire CS,
input wire RESET,
output reg [DATA_BITS-1:0] o_dat
);
reg [DATA_BITS-1:0] t_dat;
reg [DATA_BITS-1:0] mem[MEM_SIZE-1:0];
integer i;
initial
begin
t_dat = 8'd0;
o_dat = 8'dz;
for (i=0;i<MEM_SIZE; i=i+1) begin
mem[i] = 8'd0;
end
$readmemh("/home/hastings/MestProMem3/MestProMem3.srcs/sources_1/new/prog.txt", mem, 0 , 2047);
end
always @(posedge CLK or negedge RESET)
begin
if (RESET) begin
t_dat = 8'd0;
o_dat = 8'd0;
for (i=ROM_SIZE-1;i<MEM_SIZE; i=i+1) begin
mem[i] = 8'd0;
end
end
else begin
if (CS & WE & (addr>ROM_SIZE-1)) begin
t_dat = in_dat;
mem[addr]= t_dat;
end
else if ( CS & !WE) begin
o_dat = mem[addr];
end
end
end
endmodule

## Slide 3: Memory Module
Chip Select (CS)
  High (1) -> select enabled
  Low (0) -> select not enabled
Write Enable (WE)
  High (1) -> write enabled (read disabled)
  Low (0) -> write disabled (read enabled)
RESET
  High (1) -> Programmable memory set to zero
  Low (0) -> RESET disabled
  CS enable not required
  ROM not set to zero
64K Programmable Memory
2K Read Only Memory (ROM)
  Loaded at initialization/power-up
0
.
.
.
2047
.
.
.
.
.
.
.
.
.
.
.
.
.
.
65535
2K ROM
62K Programable
Memory

## Slide 4: Memory Module – Design Questions
Should a WRITE error flag be implemented
  Signal that WRITE failed due to a ROM address
  Could generalize to an ERROR flag and add initialization health check
Should RESET require CS
Should RESET be asserted as part of HALT instruction